## Slide 1
Sept. 7th, 2016
The Europa Initiative
for ESA’s M5 mission
JEM SCIENCE PLAN
Michel Blanc

## Slide 2
JEM
OVERARCHING GOALS
Provide an advanced description of Europa as a complex system of coupled layers, from core to plasma envelope, understand the role of its coupling to the Jupiter system in the potential emergence and maintenance of habitability conditions within a potential Europan biosphere, and search for signatures of life at the surface/sub-surface.

## Slide 3
JEM
SCIENCE PLAN
TWO SPECIFIC ENTRIES:
A multi-layered system, with coupling processes:
Between the layers  importance of the interfaces (ocean floor, icy shell surface)
Between Europa and the Jupiter system
A multi-scale investigation, which JEM will study at least at three characteristic scales:
Global scale;
Zoom on « potential biosphere » (ocean floor, ocean, ice shell
Zoom on local scale.

## Slide 4
… and EMFM provides information on
farther and closer
Europan environment and maps the surface at intermediate scales
JEM observing System
Orbiter
provides
global and continuous
coverage
for three
months
Lander provides
a fixed astrobiology
and
geophysics/chemistry
Station for 35 days
A « classical »
ground-space
observing system

## Slide 6
Gravity Field and
Tidal forcing
Magnetic Field and
Magnetospheric forcing
Processes at the interface layer:
Surface/exosphere/ionosphere
GLOBAL STUDY
Europan system
Response to Jupiter forcing
ZOOM ON POTENTIAL BIOSPHERE
Critical processes at the ice shell surface
FOCUS ON LOCAL SCALE
Search for signs of life
Investigation # 2
Investigation # 1
Investigation # 3
JEM OVERARCHING GOALS
AND SCIENCE PLAN
Processes at the interface layer:
Surface/exosphere/ionosphere
Investigation # 4
Search for and detect
biosignatures
Investigation # 5
Notes: FIG 6

## Slide 7
1. Static g and internal structure:
  Lateral variations, Clm Slmto degree 20+
  Improvement in vertical structure retrieval
2. Tidal response characterisation:
  g tides (k2)
  Surface tidal deformation (h2) – Altimeter!
  Global tidal heating (of ice shell)
3. Rotation-libration (gravimetry + positioning)
Gravity Field and
Tidal forcing
Investigation # 1
ORBITER | LANDER
Gravity science | Seismometer or geophone
Altimeter | Optical corner
PRIDE-E (Astrometry by VLBI) | Tlltmeter?
Major step forward in ice shell characterization
Including its
tidal interactions with Jupiter !

## Slide 8
Magnetic Field and
Magnetospheric forcing
Investigation # 2
STUDY THE 2-OBSTACLE EUROPAN MAGNETOSPHERIC INTERACTION
1. Mag flux interaction with conducting ocean
  -> separation of the 4 contributions to B field:
  Impinging magnetospheric field (about 450 nT)
  Ocean- induced currents (about 50 nT)
  Plasma currents: ionosphere, Alfven waves
  Permanent core field? (small and unknown)
2. Charged particles interaction with surface.
- > Global picture of Europan magnetospheric interaction with Jupiter for comparison with:
  Ganymede interaction (Europa-JUICE synergy)
  Other types of planetary/satellite interactions
ORBITER | LANDER
Magnetometer | Magnetometer
Plasma instrument (IMS/ELS) | Radiation monitor
NIMS? | 

## Slide 9: OUR EUROPAN « MAGNETIC OBSERVATORY »
The geometry of a halo relay orbit facilitates the separation of
the 4 contributions to the B-field
(figure from Kivelson et al., 2009)
Halo: impinging magnetospheric field
Surface:
surface field
diurnal varriation
Orbit: global
external field

## Slide 10: JEM TRACEABILITY MATRIX