## Slide 1: Europa Initiative
Sketch for a telecoms system

## Slide 2: Telecoms system functions
NASA mission phases :
  Cruise & insertion phases : comms with Earth
  Relay for lander :
    Comms with Earth
    Proximity link with lander
Complementary orbital mission
  Probe comms with Earth

## Slide 3: Telecoms system elements
Orbiter equipments
  To be designed
  To cope with :
Lander equipments
  JPL-designed
Earth ground segment
  NASA DSN

## Slide 4: Concept for orbiter/Earth comms
Proposed concept : Juno-like and DSN-compatible
X-band 2-ways link for :
  TC, HK & science TM
  Navigation (doppler & ranging)
  All mission phases
Radio-science : 2-bands system
  X-band link +
  Ka transponder (carrier-only)
Possible upgrade :
  Ka science downlink if DSN upgrades to X+Ka ground stations
  Increased data rates

## Slide 5: Orbiter equipments for Earth comms
X-band system :
  Complete RX-TX (transponder, modulation & coding, amplifier)
    Possible upgrade to higher spectral efficiency coding & modulation schemes (8-PSK, 16-APSK)
Ka band system :
  Minimum configuration : transponder for radio science
  Optional TX (modulation & coding, amplifier) for science downlink
All equipment duplicated for full redundancy

## Slide 6: Orbiter equipments for Earth comms : antennas
HGA :
  3m-diameter, >45db gain, 2-bands (X+Ka)
  For TM & radio-science during nominal mission + cruise
MGA :
  For TC function during all phases
  For TM during manoeuvers (when HGA cannot be pointed)
LGA :
  For TC/TM/navigation when MGA cannot be pointed (strong off-point manoeuvers, safe mode)
  At least 2 antennas on opposite spacecraft sides, for 4π sr coverage
All fixed antennas, pointing achieved by spacecraft

## Slide 7: Concept for orbiter/Earth comms : capacities
Budgets :
  Mass / power for minimal system (i.e. w/o Ka TM) : 90 kg / 120 W
    + Additional shielding to cope with Europa harsh radiation environment
X-band data rates :
  TC : VBR up to few kb/s (typically 2-4)
  TM : VBR up to few 100 kb/s (typically 200)
  Based on usage of NASA DSN 35m-diameter antennas

## Slide 8: Proximity link
Should this system be designed from scratch, S-band would be suggested :
  Recent trade-off for asteroid mission between UFH, S-band, X-band
  S-band : best mass/power/volume/performance compromise
But it is not!

## Slide 9: Proximity link
Lander concept features a pointed antenna
  Best compromise between data rate and power
  Probably X-band
  Orbiter comms concept : comms with Earth and lander are obvioulsy exclusive
Proposed concept :
  Using the same orbiter X-band equipments for Earth comms and proximity link
  Using LGA on orbiter to reduce spacecraft pointing requirements
Needs to download orbiter ephemeris to the lander
  1st contact may need a half-space LGA on lander

## Slide 10: Thanks for your attention! Any question?