## Slide 1: Radiation
N. André, with inputs from J. Cooper

## Slide 2: MISSION SEQUENCES
Phase 1: Interplanetary cruise
Phase 2: JOI
Phase 3: Optimized tour of Galilean satellites to first Europan working orbit
Phase 4: First Europa orbit sequence for Lander delivery (slide 24)
Phase 5: Second halo-Europa orbit sequence for Lander relay
Total lander mission duration: 20 days ?
Phase 6: Circularization to low, polar, circular orbit
Phase 7: Main orbiter mission sequence: tbd months.
Phase 8: De-orbit and descent science
End of JEM mission.
Yellow: under NASA control – Red: under ESA cotrol
Surface
science
Orbitalscience

## Slide 3: Radiation issues
Total Ionizing Dose on electronics
Signal to Noise Ratio on detectors

## Slide 4: Caution
Radiation dose estimates strongly depend on the mission profile
I will illustrate first why it is important to go quickly in low-altitude orbit around Europa
I will use radiation dose estimates for other missions to Europa for comparison

## Slide 5
This European paper gives similar 100 – 500 km orbital dosage reduction of 60 – 75 % with more sophisticated GEANT tracking code for electron motions in near-Europa magnetospheric magnetic field, Version 2.

## Slide 6
No Moon Shielding
With Moon Shielding
0.2
0.6
90-Day Europa Orbit Dose Reduction for GSFC EDGE Orbiter Study
x3

## Slide 7: Mission TID Doses @ 100-mil-Al
Jupiter Europa Orbiter (JEO) 2.9 Mrad
109 days in Europa orbit 1.25 Mrad
Moon tour 1.65 Mrad
JEO-B orbiter (1 month) 1.6 Mrad
EDGE orbiter (3 months) 2.1 Mrad (0.25 Mrad/month)
JEO-C multiple flyby 2.0 Mrad
Europa Clipper (2014 AO) 2.7 Mrad
Europa Orbiter (2014 AO) 4 Mrad (1 year in orbit,
0.25 Mrad/month
Conclusion: JEO-B (2012), EDGE (2014), and 2014 AO orbiter mission doses mutually consistent with 1.35 Mrad jovian moon tour and 0.25 Mrad/month in orbit

## Slide 8: Radiation dose for this mission
Best estimate:
  2 Mrad @100 mil Al (0.25 cm)
  300 krad @400 mil Al (1 cm)

## Slide 9
Unshielded
vs.
Moon Shielded
90-day Average Flux
x3
2014 EDGE Average Orbital Flux Model from SPENVIS

## Slide 10
Surface Energy Fluxes mW/m2
Mimas 2.5
Enceladus 0.73
Tethys 0.48
Dione 0.44
Rhea 0.29
Callisto 0.19
Ganymede 5.4
Europa 99
Cooper et al. (Plan. Sp. Sci., 2009)
Peak Flux

## Slide 11: Radiation Mitigation Strategy
Vault for subsystems including main electronics for instrument
Instrument detector heads inc. front-end electronics deported from main electronics
Very massive vault : would require a clever accomodation for all electronics